## Slide 1: 中风康复BCI实验范式
分享人：周晴

## Slide 2
机械手与openvibe解析结果是否一致、是否有延迟、是否采样精度不同？
实验范式：MI时长比例
4s
2s
1s
1s
2s
运动想象
Beep音
Cue出现
Feedback
Rest

## Slide 3: A Randomized Controlled Trial of EEG-Based Motor Imagery Brain-Computer Interface Robotic Rehabilitation for Stroke
Kai Keng Ang, Singapore, 2014

## Slide 4: A Randomized Controlled Trial of EEG-Based Motor Imagery Brain-Computer Interface Robotic Rehabilitation for Stroke
Kai Keng Ang, Singapore, 2014
Manus Intervention
  12 therapy sessions(3 times per week over 4 weeks)
    3 robot-assisted runs of 320 trials
    5 nonassisted runs of 16 trials
    amounting to 1,040 trials, lasted approximately 1.5 hours
BCI-Manus Intervention
  A calibration session
    4 runs of 40 trials
    20 trials of MI & 20 trials of idiling
  + 12 therapy sessions
    4 runs of 40 trials
    break of 3 to 5 minutes after each run
Notes: Manus：4周 3次/周，1 session/次，共12session，1.5小时/session，3+5runs/session

## Slide 5: Brain-computer interface-based robotic end effector system for wrist and hand rehabilitation results of a three-armed randomized controlled trial for chronic stroke
Kai Keng Ang, Singapore, 2014

## Slide 6: Brain-computer interface-based robotic end effector system for wrist and hand rehabilitation results of a three-armed randomized controlled trial for chronic stroke
Kai Keng Ang, Singapore, 2014
BCI-HK Intervention
  MI-BCI coupled with HK robot-assisted PP therapy(60 min)
  therapist-assisted arm mobilization(30 min)
  a calibration session(4 runs) and 18 therapy sessions
HK Intervention
  HK robot-assisted PP therapy (60 min)
  therapist-assisted arm mobilization(30 min)
SAT Intervention
  distal arm training of forearm pronation-supination movements incorporating wrist control and grasp-release of various objects (60 min)
  therapist-assisted arm mobilization(30 min)

## Slide 7: Brain-computer interface-based robotic end effector system for wrist and hand rehabilitation results of a three-armed randomized controlled trial for chronic stroke
BCI-HK intervention
  a calibration session
    MI in the first 2 runs (80 trials MI + 80 trials idle)
    PM in the subsequent 2 runs (80 trials/run)
  18 therapy sessions (six weeks)
    1 evaluation run of 40 trials with feedback (20 trials MI +20 trials idle class)
    4 rehab runs of 30 trials with feedback (MI + PP) total of 120 trials (none idle class)
    first 2 runs perform kinesthetic MI of hand grasping action subsequent 2 runs perform kinesthetic MI of knob manipulation action
    If MI was not detected in 2 consecutive trials, then the HK robot-assisted PP would be automatically initiated
Kai Keng Ang, Singapore, 2014

## Slide 8: Brain-computer interface-based robotic end effector system for wrist and hand rehabilitation results of a three-armed randomized controlled trial for chronic stroke
HK intervention
  18 therapy sessions
  the setup for the HK intervention is the same as the BCI-HK intervention
  4 runs of 30 PP trials / session
    first 2 runs hand grasping PP
    subsequent 2 runs knob manipulation PP
  If no movements from the subject were detected, the HK would initiate fully assisted PP after 2 s
Kai Keng Ang, Singapore, 2014

## Slide 9: Brain-computer interface-based robotic end effector system for wrist and hand rehabilitation results of a three-armed randomized controlled trial for chronic stroke
SAT intervention
  18 therapist-assisted sessions
  60 min of repetitive task training focusing on forearm pronation-supination movements incorporating wrist control and grasp-release of various objects
Therapist-assisted arm mobilization
  included tone management and facilitation toward normal arm movement patterns via various closed-chain functional reach activities
Kai Keng Ang, Singapore, 2014

## Slide 10: Brain-computer interface-based robotic end effector system for wrist and hand rehabilitation results of a three-armed randomized controlled trial for chronic stroke
Kai Keng Ang, Singapore, 2014

## Slide 11: EEG-Based Strategies to Detect Motor Imagery for Control and Rehabilitation
Three strategies using BCI to detect MI from EEG
  operant conditioning —— a fixed model
    (the parameters on the EEG features to extract, the features to select, and how to translate the selected features to provide feedback to the BCI user)
  machine learning —— a subject-specific model computed from calibration
    address the issue of subject training, and the high variability in EEG for single-trial data
    facilitated largely by the common spatial pattern (CSP) algorithm
    --filter bank common spatial pattern(FBCSP)
  adaptive strategy —— continuously compute the subject-specific model
    Parameters are computed from a calibration session and subsequent feedback sessions
Kai Keng Ang, Singapore, APRIL 2017
Notes: operant conditioning包含了脑电图特征提取的参数，选择的特征，以及如何翻译所选的特征来为BCI用户提供反馈。因此，研究对象必须学会控制特定的脑电图特征
CSP algorithm requires several parameters, such as the temporal frequency band-pass filtering of the EEG signals and the time segment of the EEG extracted relative to the instruction cue to the subject 自适应BCI不适合全部BCI应用，在SMR效果好，在P300等不完全适用

## Slide 12: EEG-Based Strategies to Detect Motor Imagery for Control and Rehabilitation
Kai Keng Ang, Singapore, APRIL 2017

## Slide 13: EEG-Based Strategies to Detect Motor Imagery for Control and Rehabilitation
Kai Keng Ang, Singapore, APRIL 2017

## Slide 14: EEG-Based Strategies to Detect Motor Imagery for Control and Rehabilitation
Kai Keng Ang, Singapore, APRIL 2017

## Slide 15: EEG-Based Strategies to Detect Motor Imagery for Control and Rehabilitation
machine learning strategy(a) accuracy与FMMA对照(b)
Kai Keng Ang, Singapore, APRIL 2017
Notes: 随机对照试验只做了ML组

## Slide 16: EEG-Based Strategies to Detect Motor Imagery for Control and Rehabilitation
Kai Keng Ang, Singapore, APRIL 2017
Online：machine learning Offline：adaptive strategy
Notes: 自适应策略离线分类精度的提高不一定能转化为在线分类精度的提高