## Slide 1: BCI Competition IV
2008
分享人：周晴

## Slide 2: BCI Competition IV
Data sets 1: ‹motor imagery, uncued classifier application›
  EEG, motor imagery (2 classes of left hand, right hand, foot); evaluation data is continuous EEG which contains also periods of idle state
Data sets 2a: ‹4-class motor imagery›
  EEG, cued motor imagery (left hand, right hand, feet, tongue)
Data sets 2b: ‹motor imagery›
  EEG, cued motor imagery (left hand, right hand)
Data sets 3: ‹hand movement direction in MEG›
Data sets 4: ‹finger movements in ECoG›

## Slide 3: Data sets 1 motor imagery, uncued classifier application
[64 EEG channels (0.05-200Hz), 1000Hz sampling rate, 2 classes (+ idle state), 7 subjects]
每个被试三选二（左手、右手、脚）
校准data
  2 runs 视觉提示（箭头左右下） 有标签 4s
评估data
  4 runs 声音提示（左、右、脚、停止）无标签
  运动想象和休息持续时间都在1.5s到8s之间
  每个条件的trial数不一定相等
部分数据是人工生成的
  具有特定的属性，用来评估和比较分析技术
Notes: 分类器连续地应用于传入的EEG，而不需要被试切换意图的提示。
该数据集没有提示信息。用户没有控制意图时，分类器应该返回0。
generating artifical EEG signals with specified properties that is such realistic that it can be used to evaluate and compare analysis techniques.

## Slide 4: Data sets 1 Results
性能评估：针对目标向量的均方误差（mse）
  类1标为-1 放松标为0 类2标为1
Notes: 包含开始提示后1s到停止提示
c d e 人为生成

## Slide 5
Zhang Haihong, Institute for Infocomm Research, Singapore
  Clustering after PCA or ICA to get a rest class; CSP on multiple bands; mutual information based feature selection; radial basis function based neural network
Dieter Devlaminck, University of Ghent; Psychiatric Institute of Guislain; University Hospital Ghent
  Band-pass filtering, multiclass CSP, multiclass SVM with ordinal regression, smoothing
Kai Keng Ang, Institute for Infocomm Research, Singapore
  CSP on multiple bands; mutual information based feature selection; Naive Bayes Parzen Window classifier
Data sets 1 Results

## Slide 6
Jun Lv, South China University of Technology, Guangzhou, China
  CSP-based method
Liu Guangquan, Shanghai Jiao Tong University, China
  CSP in frequency bands that were optimized by cross-validation; log-variance; LDA
Abdul Satti, University of Ulster
  Selection of frequency bands by particle swarm optimization; selection of time intervals by corss-validation; CSP with specific filter selection; log-variance; LDA; smoothing
Data sets 1 Results

## Slide 7: Data sets 2a 4-class motor imagery
[22 EEG channels (0.5-100Hz; notch filtered), 3 EOG channels, 250Hz sampling rate, 4 classes, 9 subjects]
4类运动想象（类1：左手 | 类2：右手 | 类3：双脚 | 类4：舌头）
2 sessions 视觉提示（箭头方向） 无反馈
  T打标签做训练集
  E不打标签做测试集
6 runs * 48 trials（每类12 trials）= 288 trials per session
22 EEG channels
3 monopolar EOG channels
Notes: 五分钟 ： 两分钟的眼睛睁开(看屏幕上的一个固定的十字)(2)一分钟闭上眼睛(3)一分钟的眼球运动。

## Slide 8: Data sets 2a Results
性能评估：kappa值
  如果分类是随机的，那么kappa值是0
0
1
kappa值
一致性
低
高
Notes: Kappa用来评价一个分类器的准确性，特别是在标签不平衡的状态下
kappa计算结果为-1~1，但通常落在 0~1 间，可分为五组来表示不同级别的一致性：
0.0~0.20极低的一致性(slight)
0.21~0.40一般的一致性(fair)
0.41~0.60 中等的一致性(moderate)
0.61~0.80 高度的一致性(substantial)
0.81~1几乎完全一致(almost perfect)

## Slide 9: kappa
expected probability
observed proportionate agreement
用来评价一个分类器的准确性，特别是在标签不平衡的状态下

## Slide 10: Data sets 2a Results
Kai Keng Ang, Institute for Infocomm Research, Agency for Science, Technology and Research ，Singapore
  Preprocessing: Artifact removal with bandpass filter.
  Features: Filter Bank CSP (FBCSP) using multiple one-against-the-rest classifiers.
  Classification: Naive Bayes Parzen Window classifier.
Liu Guangquan, School of Mechanical Engineeing, Shanghai Jiao Tong University, China
  Preprocessing: CSP on bandpass-filtered data (between 8-30Hz).
  Features: Log variance of best eight components.
  Classification: LDA and Bayesian classifier.

## Slide 11: Data sets 2a Results
Wei Song, Beijing Normal University, China
  Preprocessing: Downsampling, EOG removal with linear regression, bandpass filter between 8-25Hz and select channels based on a recursive channel elimination.
  Features: CSP.
  Classification: Ensemble multi-class classifier using three SVM classifiers with two hierarchies and combination through voting strategy.
Damien Coyle, University of Ulster, UK
  Preprocessing: CSP on spectrally filtered Neural Time Series Prediction Preprocessing (NTSPP) signals.
  Features: Log variance of each filtered channel is calculated with a one second sliding window.
  Classification: The best classifier among 3 variants of LDA and 2 variants of SVM was chosen for each subject individually.

## Slide 12: Data sets 2b motor imagery
[3 bipolar EEG channels (0.5-100Hz; notch filtered), 3 EOG channels, 250Hz sampling rate, 2 classes, 9 subjects]
类1：左手 | 类2：右手
5 sessions
  前两个session屏幕显示（指左或右的箭头）、无反馈
    6 runs * 20 trials（左右各10 trials）= 120 trials per session
  后三个session有反馈
    4 runs * 40 trials（左右各20 trials）= 120 trials per session
前三个session含类标签，后两个session无标签，用于测试评估
Notes: bipolar EEG channels 双极型EEG通道
3 bipolar recordings(C3, Cz, and C4)

## Slide 13: Data sets 2b motor imagery

## Slide 14: Data sets 2b Results
性能评估：kappa值
  如果分类是随机的，那么kappa值是0
0
1
kappa值
一致性
低
高
Notes: kappa计算结果为-1~1，但通常落在 0~1 间，可分为五组来表示不同级别的一致性：
0.0~0.20极低的一致性(slight)
0.21~0.40一般的一致性(fair)
0.41~0.60 中等的一致性(moderate)
0.61~0.80 高度的一致性(substantial)
0.81~1几乎完全一致(almost perfect)

## Slide 15: Data sets 2b Results
Zheng Yang Chin, Institute for Infocomm Research, Agency for Science, Technology and Research, Singapore
  Preprocessing: Artifact removal with bandpass filter.
  Features: Filter Bank CSP (FBCSP) using multiple one-against-the-rest classifiers.
  Classification: Naive Bayes Parzen Window classifier.
Huang Gan, Shanghai Jiao Tong University, China
  Preprocessing: Bandpass filtering in different frequency band, EOG removal.
  Features: Common spatial subspace decomposition (CSSD).
  Classification: LDA.

## Slide 16: Data sets 2b Results
Damien Coyle, University of Ulster, UK
  Preprocessing: CSP on spectrally filtered Neural Time Series Prediction Preprocessing (NTSPP) signals.
  Features: Log variance of each filtered channel is calculated with a one second sliding window.
  Classification: The best classifier among 3 variants of LDA and 2 variants of SVM was chosen for each subject individually.
Shaun Lodder, University of Stellenbosch, South Africa
  Preprocessing: N/A.
  Features: Wavelet packet transform using only C3 and C4. Selected frequency bands were extracted and concatenated to form a multidimensional vector.
  Classification: LDA.

## Slide 17: Download dataset

## Slide 18: PCA CSP
PCA的本质是 对角化 协方差矩阵
CSP的本质是同时对角化 两类协方差矩阵

## Slide 19: PCA
目的——“降噪”&“去冗余”
  “降噪”：使保留下来的维度间的相关性尽可能小，
  “去冗余”：使保留下来的维度含有的“能量”即方差尽可能大
协方差矩阵
主对角线上的元素是各个维度上的方差(即能量)
其他元素是两两维度间的协方差(即相关性)
降噪——矩阵对角化
  非对角线元素都为零
去冗余——舍掉对角线上较小的新方差
协方差矩阵
PCA的本质是 对角化 协方差矩阵
Notes: 方差：分散程度

## Slide 20: 白化
将一组样本的协方差矩阵转换为单位矩阵的去相关方法
  减少特征之间的相关性；
  特征具有相同的方差（协方差阵为1）
对观测信号X(t)，寻找一个线性变换W0，使X(t)投影到新的子空间后变成白化向量Z(t)，即 Z(t)=W0 * X(t)
构造白化变换矩阵：
  W0= λ-1/2UT
  λ 是特征值对角阵，U是特征向量矩阵

## Slide 21: CSP(from wiki)
两类矩阵 X1 (n,t1) X2 (n,t2)
寻找使方差(或二阶矩)的比值最大化的成分W
协方差矩阵R1 R2：
同时对角化（存在同一个矩阵P，使R1 R2 对角化）
最终结果：
其中In是单位矩阵

## Slide 22: CSP（from EEG特征提取算法文献）
原始EEG信号X（N x T）
归一化的协方差矩阵C1 C2
特征值分解
（对角化）
求和C
构造
白化变换矩阵P
特征向量矩阵U
特征值对角阵λ
变换得到S1 S2
主成分分析，得到特征值λ1 λ2
S1 S2特征向量相同
取λ1中前m个最大的特征值
λ2中前n个最大的特征值
Notes: n 通道数 t 采样点数

## Slide 23: CSP（from EEG特征提取算法文献） 多分类问题

## Slide 24: CSP（from EEG特征提取算法文献） 多分类问题

## Slide 25: CSP（from EEG特征提取算法文献） 多分类问题